CS3205-Assignment 2 : Go Back N and Selective Repeat Protocol
by CS15B049 (Lokesh Koshale)
Experiment Tables :
1. SELECTIVE REPEAT
RTT in milliseconds , RT-ratio ( retransmission ratio)
Packet length = 256 ,Window size = 25 , Buffer size = 100
1. Package Rate = 20 pk/sec
Number of packets =>	100		500		1000
Package Error rate	RT-ratio	RTTavg	RT-ratio	RTTavg	RT-ratio	RTTavg
10-3	1.000	0.0203	1.004	0.0243	1.003	0.0247
10-5	1.000	0.0225	1.000	0.0184	1.000	0.0208
10-7	1.000	0.0204	1.000	0.0212	1.000	0.0217

2. Package Rate = 300 pk/sec

Number of packets =>	100		500		1000
Package Error rate	RT-ratio	RTTavg	RT-ratio	RTTavg	RT-ratio	RTTavg
10-3	1.000	0.0221	1.004	0.0189	1.003	0.0207
10-5	1.000	0.0221	1.000	0.0197	1.000	0.0195
10-7	1.000	0.0178	1.000	0.0189	1.000	0.0193

2. GO BACK N
Window size = 25 , Buffer size = 100
1. packet rate 20 pkt/s , Packet length = 1500

Number of packets =>	100		500		1000
Package Error rate	RT-ratio	RTTavg	RT-ratio	RTTavg	RT-ratio	RTTavg
10-3	1.001	1.5684	1.102	1.4751	1.076	1.5835
10-5	1.000	1.7831	1.002	1.6587	1.001	1.6791
10-7	1.000	1.6737	1.002	1.6767	1.001	1.5966

2. Package Rate = 300 pk/sec , Packet length = 256

Number of packets =>	100		500		1000
Package Error rate	RT-ratio	RTTavg	RT-ratio	RTTavg	RT-ratio	RTTavg
10-3	1.010	0.5859	1.102	0.6424	1.076	0.6419
10-5	1.000	0.5569	1.002	0.6306	1.001	0.5948
10-7	1.000	0.5580	1.002	0.5127	1.001	0.6013

Observations :

1. Selective repeat protocol’s round trip time is lesser than Go back N protocol of same window size and same error rate. As we have to retransmit the whole window for a single packet loss in GBN.

2. As the window size increases or the error rate increase the difference of round trip time between them also increases ( when error rate is not too small or zero).

3. There is a significant increase in Round Trip time with the increase in packet length ( as in table 3 compared to others ) .

4. Generally as the error rate decreases the RTT decreases .

5. Generally more transmission ratio takes more RTT .

6. With increase in number of packets there is small increase in RTT as more chances to drop the packets.

Graphs :

from next page onwards -